## Slide 1
Minufiya University
Faculty of Electronic Engineering
Dep. of Electronic and Communication Eng.
4’th Year
Information Theory and Coding
Lecture on:
Performance Analysis of Turbo Code
Prof. Atef Abou-El-Azm
Eng. Waleed Saad

## Slide 2
Outlines
Performance analysis of Turbo Code
Limitations of Turbo code in wireless communications
Proposal on wireless communications
Proposal on multi-media applications
Frame Size
Encoder Memory Size
Encoder Output Puncturing
Number of decoder iterations
Noise level
Rayleigh fading
Unreliable channel
Changing environment
Tight timing
Small frame size
Limited bandwidth

## Slide 3
Performance analysis of Turbo Code
Frame size
The larger the frame size, the bits can be interleaved with larger distance. Thus the correlation between adjacent bits will become smaller. This will give better performance on Turbo Code in terms of accuracy.
The size of trellis formed is linearly proportional to the frame size. The complexity of the decoding algorithm is independent of the frame size.
Thus, increasing the frame size will
make the whole decoding process longer, thus increasing the latency.
10111001

## Slide 4
Performance analysis of Turbo Code
Encoder memory size
The memory size of an encoder is the number of bit/state can be stored in the encoder. In our example the encoder has a memory size of 2.
For larger memory size, Turbo Code has better performance as the coding algorithm becomes more sophisticated.
The number of state n is exponentially
proportional to the memory size m.( )
Thus, the decoding time increases dramatically with the memory size. The latency will increase exponentially too.

## Slide 5
Performance analysis of Turbo Code
Encoder Output Puncturing
If output puncturing is implemented, the code rate will be restricted to 1/2. This is useful in circumstances which the bandwidth limitation is so great that additional redundancy of code to achieve a code rate of less than 1/2 is undesirable.
However, as output is punctured, some information is loss. That means the performance of Turbo Code will decrease in general. Bit error rate (BER) will increase.

## Slide 6
Performance analysis of Turbo Code
Number of decoder iterations
Firstly, the decoder gets the systematic output and also the first encoder output, while the second decoder gets the information of the systematic output and also the second encoder output.
The first decoder does not have the information of the second encoder output in the first iterations.
The performance of the Turbo Code increases as the number of iterations increases. However, the time used will also increases linearly as the number of iterations. This increases in decoding time per bits will lead to increase in latency.

## Slide 7
Performance analysis of Turbo Code
Noise level
The most direct factor to affect the performance of Turbo Code is noise level.
Noise level can be represented by signal energy per bit to noise power spectral density (Eb/No).
The larger the Eb/No, the smaller the noise level. With more favorable environment, the BER of the Turbo Code will decrease, and vice versa.
TX
RX

## Slide 8
Outlines
Performance analysis of Turbo Code
Limitations of Turbo code in wireless communications
Proposal on wireless communications
Proposal on multi-media applications
Frame Size
Encoder Memory Size
Encoder Output Puncturing
Number of decoder iterations
Noise level
Rayleigh fading
Unreliable channel
Changing environment
Tight timing
Small frame size
Limited bandwidth

## Slide 9
Limitations of Turbo code in wireless communications
Rayleigh fading
Base Station (BS)
Mobile Station (MS)
multi-path propagation
Path Delay
Power
path-2
path-2
path-3
path-3
path-1
path-1
noise
AWGN channel
No. of iterations
BER

## Slide 10
Limitations of Turbo code in wireless communications
Unreliable channel
Fading effect due to multipath time delay and frequency selective fading has make the wireless communication channel suffer much higher noise level than the wired one which affect the BER.
Base Station (BS)
Mobile Station (MS)
multi-path propagation
Path Delay
Power
path-2
path-2
path-3
path-3
path-1
path-1

## Slide 11
Limitations of Turbo code in wireless communications
Changing environment
Besides the high noise level, its level is changing. This is due to the movement of the mobile users. This makes the communication more unpredictable which makes the code design more difficult.
Base Station (BS)
Mobile Station (MS)
multi-path propagation
Path Delay
Power
path-2
path-2
path-3
path-3
path-1
path-1

## Slide 12
Limitations of Turbo code in wireless communications
Tight timing
Voice information must arrive in time. Late coming voice will generate inconvenience to listeners.
So, turbo code with a large no. of iterations is impossible for real time communications.

## Slide 13
Limitations of Turbo code in wireless communications
Small frame size
The channel is unreliable 
large frame size means higher error, frame lost, can’t be recover ...
Real time nature 
the system can’t wait for decoder latency.
100110000111110 10101

## Slide 14
Limitations of Turbo code in wireless communications
Limited bandwidth
Wireless channel spectrum is shared among the public. Each are given a limited BW.
So, turbo code should be with a little redundancy.

## Slide 15
Outlines
Performance analysis of Turbo Code
Limitations of Turbo code in wireless communications
Proposal on wireless communications
Proposal on multi-media applications
Frame Size
Encoder Memory Size
Encoder Output Puncturing
Number of decoder iterations
Noise level
Rayleigh fading
Unreliable channel
Changing environment
Tight timing
Small frame size
Limited bandwidth

## Slide 16
Proposal on wireless communications
No output puncturing
Dynamic decoding scheme
Multiple channel transmission
Make use of existing wireless protocols
Additional interleaving
Decoding with knowledge of channel characteristics
No-puncture
BER is better
BW increases
Latency increases

## Slide 17
Proposal on wireless communications
No output puncturing
Dynamic decoding scheme
Multiple channel transmission
Make use of existing wireless protocols
Additional interleaving
Decoding with knowledge of channel characteristics
With dynamic decoding
Stop decoding once the frame is error free.
Most of frames can be recovered with iterations↓
More errors  more iterations

## Slide 18
Proposal on wireless communications
No output puncturing
Dynamic decoding scheme
Multiple channel transmission
Make use of existing wireless protocols
Additional interleaving
Decoding with knowledge of channel characteristics
If one channel becomes noisy, the whole transmission suffers.
To avoid fading channels, spread the contents over multiple channels.
TDM can be used for each channel to increase capacity over the same BW.
Turbo
Enc.
Turbo
Dec.
MUX
De-MUX
channel
Turbo
Enc.
Turbo
Dec.
channel
channel
channel
xo
c1
c2

## Slide 19
Proposal on wireless communications
No output puncturing
Dynamic decoding scheme
Multiple channel transmission
Make use of existing wireless protocols
Additional interleaving
Decoding with knowledge of channel characteristics
Replacing the convolution coding with turbo coding  interleaving in GSM can be by-passed or used for better performance.
 Digitizing  convolution coding  interleaving
Burst formatting  Ciphering  Modulation 
Digitizing  Turbo coding
Burst formatting  Ciphering  Modulation 
GSM

## Slide 20
Proposal on wireless communications
No output puncturing
Dynamic decoding scheme
Multiple channel transmission
Make use of existing wireless protocols
Additional interleaving
Decoding with knowledge of channel characteristics
The narrow band signal is multiplied by a very large BW signal called the spreading signal which is pseudo noise (PN) code.
CDMA

## Slide 21
Proposal on wireless communications
No output puncturing
Dynamic decoding scheme
Multiple channel transmission
Make use of existing wireless protocols
Additional interleaving
Decoding with knowledge of channel characteristics
The forward channel (from base station to mobile)
 The convolution code r=1/2  turbo code pun.
The reverse channel (from mobile to base station)
The convolution code r=1/3  turbo no-pun.
CDMA
Pilot, sync, traffic, paging
traffic, access

## Slide 22
Proposal on wireless communications
No output puncturing
Dynamic decoding scheme
Multiple channel transmission
Make use of existing wireless protocols
Additional interleaving
Decoding with knowledge of channel characteristics
Adding extra interleaver after MUX  correlation between adjacent transmitted bits ↓  BER ↓

## Slide 23
Proposal on wireless communications
No output puncturing
Dynamic decoding scheme
Multiple channel transmission
Make use of existing wireless protocols
Additional interleaving
Decoding with knowledge of channel characteristics
Knowledge of channel fading factor can do better encoding and improve the accuracy.
1- channel char.  BER for each ch.  noise level
2- multichannel tx.  correlation, deterioration ↓
3- weighted turbo decoding
Turbo
Enc.
Turbo
Dec.
channel
channel
channel

## Slide 24
Outlines
Performance analysis of Turbo Code
Limitations of Turbo code in wireless communications
Proposal on wireless communications
Proposal on multi-media applications
Frame Size
Encoder Memory Size
Encoder Output Puncturing
Number of decoder iterations
Noise level
Rayleigh fading
Unreliable channel
Changing environment
Tight timing
Small frame size
Limited bandwidth

## Slide 25
Proposal on multi-media applications
Self prepare